## Slide 1: Overview of CE-QUAL-W2 Version 4.5
Zhonglong Zhang, PhD, PE, PH
Portland State University
CE-QUAL-W2 Workshop
August 16 - 18, 2022
UNCLASSIFIED
UNCLASSIFIED
Environmental Systems
Modeling Team

## Slide 2: Outline
W2 version 4.5 inputs/outputs
Water quality kinetics
  State variables
  Derived variables
  WQ processes
  TDG/SYSTDG
  Bed sediment
V4.5 tools

## Slide 3: CE-QUAL-W2 V4.5 Inputs
Control file changes
    csv format
    Excel template to support develop input control files
    Excel file w2_con.xlsm  w2_con.csv
Time series file changes - csv format
Atmospheric deposition inputs of WQ state variables
Atmospheric CO2 input changes
Oxygen reaeration

## Slide 4: CE-QUAL-W2 Control File: w2_con.xlsm

## Slide 5: CE-QUAL-W2 Control File: w2_con.xlsm

## Slide 6: CE-QUAL-W2 Control File: w2_con.xlsm

## Slide 7: CE-QUAL-W2 Control File: w2_con.xlsm
Advantages
Simplified editing
No graph.npt
Easier for cutting and pasting
Simplified I/O
Files are better organized
Variable names and explanations at your fingertips
Formulae are used to assist in control file development
Disadvantages
Macro – Security
W2 GUI Interface (W2_Control) for Versions 3.7-4.2 is broken

## Slide 8: Atmospheric Deposition Inputs of WQ State Variables
Atmospheric deposition: either dry or wet deposition (rain or snow) of pollutants contribute to the mass loading of a pollutant.
Dry deposition can include dust or particle transport associated with the pollutant.
The processes of atmospheric deposition include any state variables in W2.
$atm_deposition_wb1.csv |  |  |  |  | 
Atmospheric mass input, kg/km2/year |  |  |  |  | 
JDAY | PO4 | NH4 | NO3 | LPOMP | RPOMP
1 | 14 | 0.6 | 2 | 1 | 1
100 | 16 | 0.7 | 2 | 1 | 1
250 | 18 | 0.6 | 2 | 1 | 1
365 | 14 | 0.7 | 2 | 1 | 1
400 | 14 | 0.6 | 2 | 1 | 1

## Slide 9: Atmospheric CO2 Input Changes

## Slide 10: Additional Outputs
Mass balance of TN and TP
Water body fluxes of 72 pathways
Selective withdrawal outputs in snapshot (*.snp) file
Contour plots
  Ability to generate lake contours easily (elevation vs time for temperature and DO)
  Ability to generate river contours easily (model segment or distance along river vs time for temperature and DO)

## Slide 11: Water Quality Kinetics
State variables
  New state variables: Water age, Bacteria, DGP, N2, H2S, CH4, SO4, Fe species (FEII, FEOOH), Mn species (MnII, MnO2)
Directly simulates organic carbon constituents (LDOC, RDOC, LPOC, RPOC)
Algae toxins
New derived variables: Turbidity, Secchi disk, TDG, NH3
Sediment Diagenesis updates: control file, computation efficiency
Vertical migration of zooplankton and cyanobacteria

## Slide 12: Water Quality Kinetics
General Constituents
Bacteria
CBOD
DGP, N2
TDG
Algae toxins
    H2S, CH4, SO4, Fe(II), FeOOH, Mn(II), MnO2
    Zero order
    First order
    Sediment diagenesis
Organic Carbon

## Slide 13: Water Quality State Variables
TDS
Gen1
Gen2
ISS1
ISS2
WaterAge
Bacteria
DGP
N2
H2S
CH4
SO4
Fe (II)
FeOOH
Mn (II)
MnO2
PO4
NH4
NO3
DSI
PSI
LDOM (LDOC)
RDOM (RDOC)
LPOM (LPOC)
RPOM (RPOC)
CBOD1
CBODP1
CBODN1
ALG1
ALG2
DO
TIC
ALK
LDOM-P
RDOM-P
LPOM-P
RPOM-P
LDOM-N
RDOM-N
LPOM-N
RPOM-N
MICROSYSTIN
CYLINDROSPERMOPSIN
ANATOXIN-A
SAXITOXIN

## Slide 14: Water Quality: Derived Variables
DOC
POC
TOC
DON
PON
TON
TKN
TN
NH3
DOP
POP
TOP
TP
APR
CHLA
ATOT
%DO
TDG
Turbidity
TSS
TISS
CBOD
pH
CO2
HCO3
CO3
SECCHI

## Slide 15: Water Quality: Generic Constituents

## Slide 16: Water Quality: Bacteria

## Slide 17: Water Quality: CH4, H2S

## Slide 18: Water Quality: Fe(II), FeOOH, Mn(II), MnO2

## Slide 19: Water Quality: Organic Matter (OM) Constituents
  Labile Particulate Organic Matter
  Refractory Particulate Organic Matter
  Labile Dissolved Organic Matter
  Refractory Dissolved Organic Matter
N
7.2%
P
1%
C
40%
other
51.8%

## Slide 20: Water Quality: Organic Carbon (OC) Constituents

## Slide 21: Water Quality: Algae Toxins
CTP = fraction of algal group producing toxin
β = ratio of intra. toxin mass to mass of dry weight OM
Four main toxins:
Microcystin – hepatotoxin
Cylindrospermopsin – cytotoxin
Anatoxin-a – neurotoxin
Saxitoxin – neurotoxin

## Slide 22: Water Quality: Derived Variables
Turbidity (NTU) is computed from a correlation to TSS (Total Suspended Solids)
Secchi disk (m) is computed from (light extinction coefficient)

## Slide 23: Total Dissolved Gas (TDG)
Modeling DGP (Dissolved Gas Pressure)
Modeling N2 and DO
Amount of gas absorbed by water is proportional to its partial pressure in the atmosphere (conc. = solubility factor X partial pressure)
Stream/River
Lake/reservoir

## Slide 24: Total Dissolved Gas (TDG)/SYSTDG
Dam Effects on Oxygen/Gas Transfer
  Spillways, Weirs, and Gates
SYSTDG is an Excel-based spreadsheet model used to compute TDG saturation levels in reservoir and riverine systems.
TDG production equations:

## Slide 25: Sediment Compartment
Zero order sediment fluxes
  Directly specify nutrient releases, with temperature adjustment
  Available in almost all water quality models
First order sediment fluxes
  Link fluxes to organic matter
  Limited application
Sediment diagenesis modeling
  Directly simulate the reactions in the sediment layer
Courtesy of Steven Chapra
Water Column
Active Sediment Layer
Deep Sediments
Surface cell
Bottom cell
Area

## Slide 26: Sediment Diagenesis
Inputs: csv format
Outputs: Bottom layer and averaged outputs
Improve the computations
Add SOD and sediment fluxes for all water column layers
Add initial conditions for NO3 in sediment layers
Add sediment POM (POC, PON and POP) computation
Add the correction for calculating SD_W12
Add a correction for PO4 partitioning coefficient in layer 1
Add partitioning of sediment NH4
Modify the numerical solution for CH4
Model layer

## Slide 27: Sediment Diagenesis: State Variables and Processes
Organic matter (OM) accumulates on the bottom of water bodies
Accumulated OM reactions in bottom sediment layer
  Aerobic reactions - fast
  Anaerobic reactions – slow
Sediment fluxes
  Any dissolved materials may move between water and sediment pore water
  DO from water to sediment  SOD
  Mass flux depends on concentration gradient

## Slide 28: Sediment Diagenesis: Parameters and Calibration
Complex, uncertainty in sediment diagenesis parameter values which are often expensive to obtain and are heterogeneous, can lead to longer simulation times
Seems like a lot of parameters
What do we calibrate?
  Net settling rates
  Burial rates
  Particle splits (G1, G2, G3)
  Phosphate partition coefficients.
References
  Di Toro, D.M. 2000. Sediment Diagenesis Modeling. New York, John-Wiley.
  http://www.gonzo.cbl.umces.edu/index.htm

## Slide 29: CE-QUAL-W2 Multi-Water Body Computation
Multiple waterbody simulation on multiple processors and preserving numerical precision improvements from 30-90%

## Slide 30: CE-QUAL-W2 V4.5 Tools
w2_con.xlsm – develops W2 control files
w2_v45_64.exe – reads W2 inputs and execute the model
preW2-v45_64.exe – checks all W2 input files including the control file, bathymetry file, and all boundary condition files
WaterBalanceConsole_45.exe – performs the water balance calculation
W2_Post.exe – visualizes W2 model outputs
ConverterControlFile.exe – converts a previous version (V3.7 – V4.22) W2 control files into V4.5

## Slide 31: Questions?