## Slide 1: CE-QUAL-W2 Model Outputs Overview
Zhonglong Zhang, PhD, PE, PH and Isaac Mudge, MS
U.S. Army Engineer Research and Development Center, Environmental Laboratory
CE-QUAL-W2 Workshop
August 16 - 18, 2022
UNCLASSIFIED
UNCLASSIFIED
Environmental Systems
Modeling Team

## Slide 2: Outline
Model outputs
  Time series plot output
  Spreadsheet profile output
  Water quality kinetic flux output
  Withdrawal outflow
  Water level output
  Flow balance output
  N and P mass balance output
  DSI W2Linkage File
  RESTART
Model (w2_v45_64.exe ) outputs
  w2.wrn
  W2.err
  W2ErrorDump.csv
Preprocessor (preW2-v45_64.exe ) outputs
  pre.opt
  pre.wrn
  pre.err

## Slide 3: TSR Plot – Time Series Output Plot
A time series output file (csv) at a user specified segment for
Flow
Temperature
Active constituent concentrations
Derived constituent concentrations
Instantaneous kinetic flux rates (kg/d)
Instantaneous algae growth rate limitation fractions for P, N, and light [0 to 1] for each algal group.

## Slide 4: TSR Plot – Time Series Output Plot

## Slide 5: SPR Plot – Spreadsheet Output
A spreadsheet profile output file (spr.csv) consists of variable name, Julian date, depth below water surface, elevation, and temperature and/or concentrations for the output segment.

## Slide 6: Fluxes – Water Quality Kinetic Flux Output

## Slide 7: Kflux-wb: kflux_wb#.opt
Kflux-wb output option writes individual mass fluxes, sequentially, in 2-dimensional blocks of data for each time interval for active segments and layers

## Slide 8: Waterbody Flux Output: flx_wb#.csv
flx_wb output files include the waterbody-specific detailed mass balances for water quality constituent fluxes at the same level of temporal detail as CPL output.

## Slide 9: Withdrawal Output – WITH OUTPUT
qwo_#.csv
cwo_#.csv
dwo_#.csv
two_#.csv
QWO/TWO/CWO/DWO withdrawal output files include discharge/ temperature/ concentration/ derived concentration of selected segments or at hydraulic structure segments

## Slide 10: Water Level Output
wl.csv

## Slide 11: Flow Balance Output: flowbal.csv
flowbal output file list all flow balance parameters, such as volume in, out, etc.

## Slide 12: N and P Mass Balance Output: massbal.csv
This output option writes a summary of the N and P mass balance for each waterbody - cumulative N and P mass balance for all N/P sources/sinks.
Derived variables (TN, TP) are turned ON
CPL output is turned ON
MBC - mass balance is turned ON
NPBALC is turned ON

## Slide 13: N and P Mass Balance Output: massbal.csv

## Slide 14: Contour Plot Output: CPL PLOT
The CPL output file stores detailed output for all model segments (and layers) within each simulated waterbody and provide the information needed for developing both temporal and spatial model-data comparisons.
The CPL output file writes data in 2-dimensional blocks for each output time interval by combining the sequence of segment and layer results in the vertical dimension (down) and the selected output variables in the horizontal dimension (across).

## Slide 15: W2Post – XXX.w2l

## Slide 16: W2Post: Color Contour Plots

## Slide 17: W2Post: Time Series Plot

## Slide 18: W2Post: Animation

## Slide 19: W2Post: Bathymetry Data Viewer

## Slide 20: Restart and Snapshot Print
RESTART
SNP PRINT - Snapshot print

## Slide 21: Runtime Errors: w2.err

## Slide 22: Runtime Warnings: w2.wrn

## Slide 23: pre.opt: Meteorological Data Summary

## Slide 24: pre.opt: Summary Statistics
Summary statistics regarding inflows, temperatures, and inflow constituent concentrations

## Slide 25: pre.opt: Summary Statistics
Summary statistics regarding inflows, temperatures, and inflow constituent concentrations for each branch and summed for each waterbody

## Slide 26: pre.opt: Summary Statistics
Summary statistics regarding inflows, temperatures, and inflow constituent concentrations

## Slide 27: pre.opt: Area-Volume-Elevation Table
Computed area-volume-elevation table, theoretical hydraulic residence at each elevation is included if the waterbody is a reservoir

## Slide 28: Questions?